## Slide 1: Tutorial: Introduction to Verilog

## Slide 2: iVerilog & GTKWave (Windows)
Icarus Verilog for Windows:
  http://bleyer.org/icarus/
GTKWave examples:
  https://iverilog.fandom.com/wiki/GTKWave

## Slide 3: iVerilog & GTKwave (Linux)
iverilog is a compiler that translates Verilog source code into executable programs for simulation, or other netlist formats for further processing. The currently supported targets are vvp for simulation, and fpga for synthesis.
vvp is the run time engine that executes the default compiled form generated by Icarus Verilog. The output from the iverilog command is not by itself executable on any platform. Instead, the vvp program is invoked to execute the generated output file.
Install:
apt install iverilog gtkwave
compile and generate triangle.out
iverilog -o triangle.out testfixture.v triangle.v
execute and generate dump.vcd
vvp triangle.out
Display wave
gtkwave dump.vcd

## Slide 4: Cell based IC designed flow

## Slide 5: C Code vs Verilog

## Slide 6: Basic Layout of Verilog
Modules communicate externally with input, output and inout ports
A module can be instantiated in another module
module module_name( input/output port);
//Port declaration
input xxx;
output xxx;
//Reg or wire declaration
reg xxx;
wire xxx;
//continuous assignment
assign xxx = OOOOOO;
always@(sensitive list w/ edge trigger) begin
Sequential logic
end
always@(sensitive list ) begin
Combinational logic
end
endmodule
/* sample code FA_MIX.v */
module FA_MIX (A, B, CIN, SUM, COUT);
input A, B, CIN;
output SUM, COUT;
reg COUT;
reg T1, T2, T3;
wire S1;
xor X1 (S1, A, B); // Gate instantiation
always@ (A or B or CIN) // Always Block
begin
  T1 = A & CIN;
  T2 = B & CIN;
  T3 = A & B;
  COUT = (T1 | T2 | T3);
end
assign SUM = S1 ^ CIN; // Continuous assignment
endmodule

## Slide 7: Keywords
Note : All keywords are defined in lower case
Examples :
  module, endmodule
  input, output, inout
  wire, reg
  integer, real, time
  posedge, negedge
  not, and, nand, or, nor, xor
  parameter
  begin, end
  if .. else, case … endcase (mostly used)
  while, repeat, for loop (mostly used in test pattern)
  $finish, $display, $monitor
Note: anything start with $ is a system syntax, not used in design.

## Slide 8: Module Instantiation
module dff (clk, d, q);
input clk, d;
output q;
reg q;
always @(posedge clk) q = d;
endmodule
Call by order
Call by name
wire clk_i;
wire input, output;
dff f1(clk_i, input, output)
wire clk_i;
wire input, output;
dff f1(.clk(clk_i), .d(input), .q(output))

## Slide 9: Integer Constant Numbers
Format :
  <size>’<base><value>
  ’<base><value>
  <value>
Example : 4’d16 , 4’b0001 When <size> is less than <value> , the upper bits are truncated.
If grater , it will extend.
  2’b1101 => 2’b01
  4’b01 or 4’b11 => 4’b 0001 or 4’b0011

## Slide 10: Parameters
Parameters are not variables, they are constants.
Can be modified at compilation time
parameter IDLE = 4’d0;
parameter RIGHT_SHIFT = 4’d1;
parameter LEFT_SHIFT = 4’d2;
always@(*)
If(cur_state==IDLE)
…

## Slide 11: Operators[1/3]

## Slide 12: Operators[2/3]
Notes: == 值相等 1 == 1 不能->x==x
=== 意義相等 x === x
~^ xor

## Slide 13: Operators[3/3]
EX : A={B,C,D};
Ex : A=(set==1)?B:C;
A is 16 bits, B is 8 bits, C is 6 bits, D is 2 bits
A = {B,C,D} or
A = {4’d0, B[7:3], C[5:1], D[1], 1’d0}

## Slide 14: Bit extraction and Combination

## Slide 15: Partial bit operation
31:24 | 23:16 | 15:8 | 7:0
little endian
big endian
31:24
23:16
15:8
7:0

## Slide 16: wire & assign
wire
  Physical wires in a circuit
  Cannot in left hand side of assignment in always block
  Wire doesn’t store its value
  Input, output, and inout default wire data type
assign
  Models behavior of combinational logic
  Assign a value to a net using continuous assignment
  Left hand side of continuous assignment cannot be register type
assign out = ( sel )? A : B;
assign outbar = ~out;

## Slide 17: reg & always block
reg
  Variable in verilog
  Manipulated within behavior modeling(always block)
  In always block, only can use reg on left hand side of assignment
“reg” data type isn’t exactly synthesized to a really register
  reg z;
  always @(sel or a or b) begin
  if(sel)
  z = b;
  else
  z = a;
  end
Sensitive list: put all signals which affect output,
can use * to let compiler help
  wire z;
  assign z = (sel)?b:a;
Sensitive list must be specified completely,
otherwise behavior may mismatch with simulation

## Slide 18: Register
Register(Flip-flop) is implied when use @(posedge clk) or @(negedge clk) in an always block
  reg out;
  always @(posedge clk) begin
  out <= a*b;
  end
X
a
out
b
clk
input Din, clk, rst;
output reg Dout;
always @( negedge rst or posedge clk ) begin
if ( !rst )
Dout <= 1’b0;
else
Dout <= Din;
end
Din
CLK
Dout
Reset
DFF

## Slide 19: Conditional Statements

## Slide 20: Avoid Inferred latch
Inferred latch generate by compiler
Variable assigned within always block that isn’t fully specified
case (expression)
alter_1, alter_2: stm_1;
alter_3: stm_2;
…
default: default_stm;
endcase
  always @( a, b ) begin
  if( a ) begin …; end
  else if ( b ) begin ; end
  else begin …; end
  end
input [1:0] sl;
output reg [3:0]out;
always@(sl) begin
case (sl)
2’b00: out = 4’b0001;
2’b01: out = 4’b0010;
endcase
end
Why inferred latch is bad
when b=1x, out=out => generate latch
Notes: Always block
Flip flop: Event-expression contain posedge or negedge
Combinational logic: not contain posedge or negedge
Latchs: variable assigned within always block that isn’t fully specified

## Slide 21: Blocking vs Non-Blocking
A
B
C
X
+
temp
temp_c
output

## Slide 22: Blocking vs Non-Blocking
A
B
C
X
+
temp
output

## Slide 23: Nested module
multiplier
input2
input1
sel
clk_i
Reset_n
mux
adder
selected
added
multiplied